## Slide 1: CSE 3666 Exam 1 Review
The exam will cover the topics from Lectures 1.1-1.9.

## Slide 2
Numbers, bits, bytes, and ASCII characters
Binary numbers, two’s complement numbers, hexadecimal numbers.
Conversion between different number systems, including decimal numbers, binary, hexadecimal.
Signed and unsigned extension.
Addition/subtraction of binary/two’s complement numbers. Negate a two’s complement number.
Bitwise logical operations.
ASCII characters.

## Slide 3
Instruction class | RISC-V examples
Arithmetic | add, sub, addi…
Data transfer | lw, sw, lb, lbu, sb lh, lhu, lui…
Logical | and, or, xor, andi, ori, sll, sra…
Cond. Branch | beq, bne…
Jump | Jal, jalr…
RISC-V ISA
Skill: Be extremely familiar with a set of core MIPS instructions, understand their operations, and use them properly.
RISC-V instructions sets. Arithmetic, logical, memory, control flow instructions.

## Slide 4
Data
Skill: Properly specify operands in instructions and access data in programs.
1. Accessing data in registers and memory.

## Slide 5
Array in memory. Array of words, half-words, and bytes (characters).

## Slide 6
Data of different sizes. Sign extension. Endianness.

## Slide 7
addi x5, x0, 0x0C4 addi x5, x5, 4 lb x7, 0(x5)
Address . . . . . . 0x000000C4 0x456A789B
0x000000C8 0xDB733A56
. . . . . .

## Slide 8
Control flow
Skill: given enough information, encode MIPS instruction with 32 bits and understand encoded instructions.
Program counter.
RISC-V support for if-then-else, loops, functions.
Compare values with beq,bne, etc.
RISC-V calling convention. Caller-saved /callee-saved registers. Passing parameters to / returning value from functions.
Stack. Push/pop. Save/restore registers on stack. Allocate storage space on stack.

## Slide 9: Stack operations
# pop x2
lw x2, 0(sp)
addi sp, sp, 4
x1
sp
sp
sp
Push
x1
x2
sp
Pop
x2
x2
#push x1
addi sp, sp, -4
sw x1, 0(sp)

## Slide 10: push multiple words
Write RISC-V instructions to push s1, s2, and s3 onto the stack
Instead of 3 ADDI’s, we can adjust sp once for three words
# reserve space for 3 words
addi sp, sp, -12
sw x1, 8(sp)
sw x2, 4(sp)
sw x3, 0(sp)
 | Address | Value
 | 0x7FFF 901C | 
 | 0x7FFF 9018 | 
 | 0x7FFF 9014 | 
 | 0x7FFF 9010 | 
 | 0x7FFF 900C | 
 | 0x7FFF 9008 | 
 | 0x7FFF 9004 | 
 | 0x7FFF 9000 | 
sp
Before push
sp
x1
x2
x3
x1
x2
x3

## Slide 11: push multiple words
Write RISC-V instructions to push s1, s2, and s3 onto the stack
Instead of 3 ADDI’s, we can adjust sp once for three words
# pop x1, x2, and x3
lw x1, 8(sp)
lw x2, 4(sp)
lw x3, 0(sp)
addi sp, sp, 12
 | Address | Value
 | 0x7FFF 901C | 
 | 0x7FFF 9018 | 
 | 0x7FFF 9014 | 
 | 0x7FFF 9010 | 
 | 0x7FFF 900C | 
 | 0x7FFF 9008 | 
 | 0x7FFF 9004 | 
 | 0x7FFF 9000 | 
sp
Before pop sp
x1
x3
x1
x2
x3
x2

## Slide 12
Instruction Encoding
Six instruction formats.

## Slide 13
12
x
h
h
h
h
h
h
l
l
l
l
0
s
11
0
10
5
4
1
s
h
h
h
h
h
h
l
l
l
l
x
imm[31:13] are s.
Sign extension!
Instr[31:25] funct7=0 000110
imm[12:1] are Instr[31:25,11:7]
Instr[11:7] rd= 01000
Instr is the 32-bit machine code.
imm == offset
ss…ss
imm[0] is always 0
imm
31
Bne x10, x11, 200
imm
rs2
rs1
funct3
imm
opcode
7 bits
7 bits
5 bits
5 bits
3 bits
5 bits
Opcode=1100011; funct3=001;
200= 0b 0000 0000 0000 0000 0000 0000 1100 1000

## Slide 14
Assembly code
Translate pseudocode or simple C code to RISC-V assembly code.
Understand/debug RISC-V code.